## Slide 1: Energy Models

## Slide 2: Overview of Energy Models
  Trend
  Time Series
  Guess based on experience
  Survey Based
  Scenario Planning
  I/O Models
  Energy Balance Models
  Game Theory
  Experimental/Behavioral

## Slide 3: Trend
  Uses only patterns of the past to make forecasts about the future.
  Cram a line though the data.

## Slide 5: Trend Comments: General
  Regression with time as RHS variable.
  Other variables are often added, for example, weather variables. You can see this in some integrated resource planning models.
  EC469 shows you how to do this.
  Not everything is a line. You sometimes have to transform the data, logs and such are common.

## Slide 6: Trend Comments: Problems
  Only uses the past and does not show turns in trend.
    I was 90 lbs at 15, 110 at 17, 130 at 18 and 220 at 26.
    Today?
  People don’t react to prices and there is no change in technology.
    See the coal data at the end. That is the natural gas fracking boom.

## Slide 7: Trend Comments (Con’t)
  Growth of a subset can only exceed that of a superset for a while.
    Facebook can only grow faster than the US, or world, economy for so long.
  Advantages
    That said, it works for a lot of things and work when you have little time.
    Plenty of energy modeling looks like this.
      “If you don’t have the time, throw in a trend line.”
    For looking a few periods into the future – it works. For longer term forecasts – don’t do it.

## Slide 8: Time Series
  Similar to trend only
    May have
    or include a trend
    the AR part is past values of LHS
    the MA part is past values of error term.
  EC 472 shows you how to do this.
  Most energy data has a trend to it, which must be included in the model.

## Slide 9: Time Series (for now)
  Best thought of, for now, as a refinement to the trend regressions with better treatment of residuals.
    More accurate confidence intervals on existing data.
    Slightly better with near-term forecasts.
  Similar problems as pure regression on trend.

## Slide 10: There is way more to time series
  Macro is heavy into this.
  You may see macro heavy energy papers with Vector Autoregressions (VARs) which looks at many time series at once.
  Nice example of quick use by Borenstein about the California Cap and Trade (https://ei.haas.berkeley.edu/research/papers/WP281.pdf)
    They produced the key result that the price will not be at a bound, upper or lower, only 19% of the time.
    Quick analysis.

## Slide 11: Guess based on experience
  Don’t laugh, this works.
  Old hands make very good guesses based on experience.
  GDP even has components that are based on analyst’s best judgment.
  This can be combined with incentivised polls or parimutuel betting to make it work better.
    The Iowa Electronic Markets are a common example, though there are others. https://tippie.biz.uiowa.edu/iem/markets/

## Slide 12: Incentivized Polls
  Guess Jamie’s BMI. Closest to the actual gets $1.
  Skin in the game gives incentive for more thought.
  Only works when you will eventually find out actual.

## Slide 13: Incentivized Polls (Con’t)
  Oddly works better if you don’t know how people are betting.
    Can produce group-think bubbles, if you see how others are betting.
    Easy to find the mode, but harder to tell if it is real.
  Can get expensive with many winners:
    everyone guesses the same correct answer.
    More expensive when there is less certainty.

## Slide 14: Parimutuel Betting
  Guess Jamie’s BMI. Correct answers split the pot with the others that got it right.
  Racetrack method.
  Less likely to get bubbles, but
    Harder to see if there is a mode in the guess.
  Cheaper than incentivized poll if high probability of multiple winners.
  Cost does not increase with a priori certainty.

## Slide 15: Survey Based
  Book gives some examples.
  Ask a bunch of experts about their best judgement and summarize
  Often expanded as a Delphi Survey
  For comically bad forecast see “Results of the Delphi IX Survey of Oil Forecasts” California Energy Commission, 1997.

## Slide 16: Delphi Surveys
  Ask each person in private for best guess.
  Compile results.
  Ask outliers why they said what they did.
  Give everyone:
    The distribution of guesses for each parameter
    The reasons the outliers gave for the answer the gave.
  Ask for another guess.
  Report the new distribution or repeat if desired.

## Slide 17: Bayesian Truth Serum
This works best with multiple choice questions
The idea is that if you hold a particular belief, you are more likely to think that others agree.
  Ask each person what they think is most likely.
  Ask them about what others think – the probability distribution.
  Do some Bayes law majik.

## Slide 18: Scenario Planning
  Too much variation to give one description.
  General Steps:
    Choose some parameters of interest, e.g., environmental activism, sea level rise, fracking shown to cause earthquakes, etc.
    Package them into narratives that are possible. Some improbable and some likely.
    Decide how you would act now given that you know that that future will exist.
    ?
    Profit

## Slide 19: Example Scenario Planning
  Example by National Renewable Energy Research Laboratory (NREL) did one for Hawaii. http://www.nrel.gov/docs/fy12osti/52442.pdf
    Contractor reports tend to go long.
    See page 6 for summary of the scenarios.
    Contractor reports tend to use lots of acronyms.
    Plug in Hybrid Electric Vehicle (PHEV)

## Slide 20: Frequent use and abuse of scenarios analysis
  Rigging scenarios so that only one is taken seriously. (abuse)
  Choosing actions that will “work” in all scenarios. (abuse)
  Actual plans if a scenario becomes more likely, “Plans are worthless, but planning is everything.” - Ike

## Slide 21: Better use of Scenarios
  Creation of real options
    Defer action until more information is available. Don’t bring an umbrella everywhere, but have on near by if it starts to rain.
    Create systems you can use when the situation is clearer. Think peaking power plants that only run a few days a year.

## Slide 22: I/O Models
  Old school – 1920s Leontief
  Has an equilibrium concept
  Assumes fixed ratios are used in production
    No reaction to price changes
    No reaction to input price changes
    Constant returns to scale.
  Often seen as part of a computable general equilibrium model to shorten run-times. REMI (http://www.remi.com/) and IMPLAN (http://implan.com/) use it in regional economic models.

## Slide 23: Walk Through I/O model
  is how much of good one that gets made.
  is how much final consumers want of good 1.
  the amount of good 1 needed to produce good 1.
  the amount of good 2 needed to produce good 1.
  Each good has an equation
  s can be zero but The matrix needs to be invertable.

## Slide 24: I/O in Matrix Form
is solved as
d is what you need to fight the war. X is what you need to produce to get d.

## Slide 25: Warnings about the next models in book
  They are an unholy mix of estimates, in engineering sense, and estimates, in the statistical sense.
  They can be huge. The national energy modeling system has many modules and sub-modules.
    http://www.eia.gov/forecasts/aeo/nems/overview/electricity.html
  The approaches are frequently combined.

## Slide 26: “Estimate” to an Engineer and Statistician
  To an engineer, an estimate means taking some known or assumed values for parameters then performing some calculations to find a parameter of interest.
    Example, building energy simulations like EnergyPlus. Put in windows, screens, walls, assume some values human behavior, and weather and out pops annual energy use.
    Can work with very complex models, but is usually shaky with uncertainty.

## Slide 27: The statistician
  To a statistician, an estimate means taking data, repeated observations of a physical data generating process and calculating a summary statistic.
    Example, estimate implied thermostat settings from gas use and R values of walls from a survey.
    Treats uncertainty well but often lack the complexity of the engineering style models.

## Slide 28: Combining Engineering and Statistician Style Estimates
  A typical Example is estimates of Unit Energy Consumption (UECs)
    The EIA Residential Energy Consumption Survey (RECS) http://www.eia.gov/consumption/residential/reports/2009/methodology-end-use.cfm
    California Residential Appliance Saturation Study (RASS) https://www.energy.ca.gov/data-reports/surveys/2019-residential-appliance-saturation-study

## Slide 29: Combining engineering estimates
  Check the details for RASS and see how they combine engineering estimates with regression analysis.
    https://www.energy.ca.gov/sites/default/files/2021-08/CEC-200-2021-005-MTHLGY.pdf.
    Often called a statistically adjusted engineering model.

## Slide 30: Game Theory
  Not a full, all economy, model but a tool used to deal with decisions where:
    There is not a monopoly or monopsony.
    Not perfect competition.
  Also used for:
    Dynamic interactions of firms, think how gasoline prices go up fast but down slow.
    Auction and bidding, technically mechanism design which is game theory backwards, to get people to tell the truth or do the right thing.
    Basis for a lot of modern “regulation” which focuses on encouraging competition to reach goals.

## Slide 31: Experimental/Behavioral
  The behavioral part is admitting that people and firms do not act rationally.
  Old school experiments, A/B testing and more, run on people
  Field experiments are common in economics now
    Esther Duflo received the Bates Clark Award 2010
    Bluffstone and others in Econ is running two now in Ethiopia and Nepal.

## Slide 32: Typical Issues
  Internal validity
    Can you really connect cause to effect?
    Did you avoid bias and control for everything?
  External validity
    Does it work in real life?
    Does it work on other people?
  Ecological validity
    Did the experiment look like the real world?

## Slide 33: Overarching
  Every model is wrong
    By definition they are simplifications of reality and they leave out details.
    The real question is, “Did they leave out the right details?”
  Don’t be deluded into, “Just look at the data”.
    You come to data with a model, you just don’t know it.
    The data never speak for themselves. You use data to test/support/refute hypotheses/theories.

## Slide 34: Overarching (Con’t)
  Using more than one model or technique and getting the same general result helps. It shows that your conclusion about reality is resilient to the implicit modeling assumptions.

## Slide 35: Overarching (Con’t, Con’t)
  Keep in mind that modeling is an iterative process often driven by the researcher.
    You try a model and then refine it based on the results.
    It is an iterative process.
    Your choices are molded by your objectives. “Get published” is common.

## Slide 36: P-Hacking
Great working paper on this by Gelman that expands on this idea “The garden of forking paths: Why multiple comparisons can be a problem, even when there is no “fishing expedition” or “p-hacking” and the research hypothesis was posited ahead of time" (http://www.stat.columbia.edu/~gelman/research/unpublished/p_hacking.pdf)